## Slide 1: illbruck Projecting Window System (PWS)
New 2014: PR010 window mounting angle,
PR011 window mounting panel, PR012 insulating block
Simon Pronath, Product Management CEU

## Slide 2
PR010 window mounting angle

## Slide 3
    ift component test
    from 50 mm plate
    projection 120 / 140 / 160 / 180 / 200 mm
    120 mm high
    length: 1400 mm
    weight: 5,8 – 7,5 kg/m
    manufactured to order
    delivery time 8 days
    PR012 insulating block
      possible
PR010 L-shape angle

## Slide 4
illbruck projecting window system
4
flexibility
tasks:
projection 35, 90, 120, 140, 160, 180, 200 mm
large packets
order-related quantities
equipment edit

## Slide 5
illbruck projecting window system
New PR010 angle 120 mm
5
PR011 panel 35er
PR007 frame 90 mm
PR008 insulation wedge
PR010 L-angle 120 mm
PR012 insulating block
PR010 L-angle 140 mm
PR012 insulating block
PR010 L-angle 160 mm
PR012 insulating block
PR010 L-angle 180 mm
PR012 insulating block
PR010 L-angle 200 mm
PR012 insulating block

## Slide 6
PR010 angle load capacity
presentation
bonded to concrete
bonded to bricks
presentation
bonded to limestone
bonded to aerated concrete

## Slide 7
PR007 frame and PR010 angle
load capacity
refers to 1 meter frame
with 7-fold safety
with 3-fold safety for artificial aging
for not requiring authorization systems
breaking load is about 10-fold higher
The load figures shown were obtained with an assumed min. 7-fold safety and reduction of the long-term stress according to the ift VE-08 determined. The loads were extrapolated from 10 cm to 100 cm widths experimental angles.

## Slide 8
window 1.30 x 1.70 m with 3-fold glass on calcareous sandstone with 160 projection
calculate weight of the window, page 104 + 112 in the LZM = 90 kg
set substrate = limestone
set type and projection = 160 mm
see table = 149 kg/m
static calculation: 149kg/m x 1,30 m = 193,7 kg load transfer only below!
Static is sufficently dimensioned, like this example 90 kg < 193,7 kg
PR007 frame and PR010 angle
load capacity - example

## Slide 9
PR011 window mounting panel 35 mm

## Slide 10
    ift component testing
    from 35 mm plate
    35 mm projection
    90 mm high
    Length: 1400 mm
    Weight: 1,8 kg/m (PR007 2,7 kg/m)
    manufactured to order
    delivery time 8 days
PR011 panel 35 mm

## Slide 11
benefit edge distance
Choose edge distance independet of the masonry
Annulment the manufacturer's specifications by a "security" with Purenit strip
Hochlochziegel, MW-Abstand ca. 10 cm
Beton, MW-Abstand < 5 mm
KSV, Abstand MW ca. 10 mm
PR011 panel 35 mm

## Slide 12
sound insulation

## Slide 13
Question: what is the difference of sound insulation in various installation situations?
illbruck projecting window system
sound insulation

## Slide 14
What we know:
illbruck projecting window system
sound insulation

## Slide 15
What we‘ve tested:
illbruck projecting window system
sound insulation

## Slide 16
ift-testing for illbruck projecting window system
soundproof window with 43 ​​dB (without sound side paths!)
combination window 43 dB + PWS + TP652 + SP525 inside = 43 dB.
does not reduce the rated sound insulation value of the window (this is the value that sound-proof windows without sound side paths reaches maximum)
16
illbruck projecting window system
sound insulation
PR011 and PR007

## Slide 17: illbruck projecting window system sound insulation PR010 window mounting angle

## Slide 18: illbruck projecting window system sound insulation PR010 window mounting angle PR010 window mounting angle

## Slide 19: illbruck projecting window system sound insulation PR010 window mounting angle result

## Slide 20: illbruck projecting window system sound insulation PR010 window mounting angle
developed conversion table

## Slide 21
New from June 2014
Summary

## Slide 22
illbruck projecting window system
22
PR010 angle in 120 mm projection (120 to 200 mm
new processing movies on the internet
    https://www.youtube.com/watch?v=P9N-E5_qdNU
    https://www.youtube.com/watch?v=e43vUq2nS5o
    https://www.youtube.com/watch?v=10sZqxjJn7A
new load transmission table in the data sheet
All types make to order  short delivery times
new brochures 20 pages
PWS price list with consumption calculator (SU Germany)
Hand sample for PR011, PR007, PR010 angle and panel at the post office

## Slide 23
Burglar Inhibition
according to RC2 und RC3 (old WK2 and WK3)
DIN EN 1627-1630

## Slide 24
an genau definierten Punkten wird eine Kraft (mit Hydraulikzylinder) kontinuierlich aufgebaut. RC3 = 6.000 N (6 kN)
Pendelschlagversuch von außen(!) 50 kg. RC 3 = 750 mm Fallhöhe
Angriffszeit 5 Minuten Werkzeug: Schraubendreher, Kuhfuß
Basics RC3
Notes:  bestanden, wenn sich keine Spaltlehre in eine Öffnung schieben lässt (das ist ein Rundstahl mit 10 mm Durchmesser und 200 mm Länge mit Griff

## Slide 25
PR010 Fenstermontage-Winkel 200 mm projection
    Ø 7,5 mm Sicherungsschrauben: below 3, side/top á 1 = 6 Stück
IV 68 timberframe RC3; size: 1,23m x 1,48 m
    Ø 7,5 mm Rahmenschraube: side á 4, top 3 = 11 Stück
TP652 trioplex+ 66/7-15
Mock-up RC3
Notes: Abdichtung/Befestigung unten:
Fenster „knirsch“ in eine Raupe SP340 auf PR010 gesetzt

## Slide 26
Special feature of our test:
illbruck projecting window system
RC2 und RC3 System-Testing
We also between the frame and angle: Simulates the attack during the construction phase in the “not yet covered” state.
manual attack usually only between frame and window:
Both is possible with PWS!

## Slide 27
Manual attack frame-winow manual attack frame-PR010
illbruck projecting window system
RC2 und RC3 System-Testing

## Slide 28
Result RC3
Notes: Das PIV in Velbert ist ein renommiertes und akkreditiertes Prüfinstitut für Beschlags-Technik.
Vorprüfung war bei WINK HAUS in Telgte.
Wir können sagen, dass wenn das Fenster selbst RC3 hat, es auch in unserem Vorwandmontage-System Typ 3 (120-200mm Ausladung) verbaut werden kann.
Typ 1 + 2 müssen erst noch (evtl. gutachterlich) überprüft werden.

## Slide 29
Thank You!
Simon Pronath
Product Management Central Europe
tremco illbruck GmbH & Co. KG
Von-der-Wettern-Str. 27
51149 Köln
T: +49 2203 57550-227
frank.woermann@tremco-illbruck.com
Info.de@tremco-illbruck.de
www.tremco-illbruck.de